## Slide 1: World federation of neuroscience nurses
Managing External Drainage of CSF:
Practical tips for nursing care

## Slide 2: Objectives
To provide an overview of basic principles of CSF diversion including the following:
  Indications for CSF drainage
  Types of CSF diversion systems
  Nursing care and management of EVD’s and lumbar drains

## Slide 3: Why do we drain CSF?
To treat high pressure states in selected patient
  Control elevated intracranial pressure by draining CSF
  Normal Pressure Hydrocephalus
  Obstructive hydrocephalus
  Communicating hydrocephalus
To treat or prevent leaking of CSF when the dura has been surgically opened
Shunt infections (externalize drainage while treating infection)

## Slide 4: Options for CSF diversion

## Slide 5: What is an external ventricular drain (EVD)?
A drain that is placed surgically into the ventricles
Generally tunneled and sutured to the scalp
  Always document the opening pressure if performed at bedside
Allows CSF to drain into a sterile bag
Can be helpful in treating:
  Elevated intracranial pressure
  Diverting CSF to treat an infection
  Clearing blood products from the ventricles

## Slide 6: External ventricular drain nursing care
Level the drain to ordered level
Observe drainage hourly
Call a supervising provider for drainage less than or more than expected values
If transduced, treat elevated ICP by opening the drain when the pressure exceeds the prescribed level

## Slide 7: External ventricular drain nursing care
Clamp if out of bed/ re-level with bed adjustment
CSF sampling is no longer considered standard of care
Dressings have not been found to reduce the risk of infection
Observe insertion site for signs infection or CSF leakage

## Slide 8: What is a lumbar drain?
A closed sterile drain system that is placed in the subarachnoid space to drain CSF
Generally placed at L3-4 (spinal cord ends at T12-L1)
Common indications include:
  Diagnostic evaluation of idiopathic intracranial HTN
  Diversion of CSF after dural tear or CSF leak
  Diversion during treatment of a shunt infection
  Thoracolumbar aortic aneurysm to improve spinal cord perfusion

## Slide 9: Lumbar drains nursing care
Level the drain to ordered level
Observe drainage hourly
Call if drainage exceeds or is less than expected values
Educate the patient to call for help before getting out of bed (clamp drain)
Re-level with any bed adjustment

## Slide 10: Lumbar drains nursing care
Consider restraints/family sitter if unable to follow instructions
Transparent dressings should be in place and observed every shift
Avoid contamination during peri-area care
If required, dressing changes should be sterile
Observe insertion site for signs infection, leakage of CSF

## Slide 11: Sampling CSF for culture (example)
ALWAYS follow your hospital procedures
Don clean gloves, mask
Prep side port below the buretrol with two betadine prep pads and allow to dry 3 minutes (ensure sampling port remains sterile)
Insert needle into side port below the buretrol port and withdraw sample at least of 1 ml of CSF
Replace needle with sterile blue cap
Label specimen with date/time collection and nurses signature
Send to lab for analysis with lab requisition

## Slide 12: Nursing care of the all CSF drains
Assess insertion site every four hours for signs/symptoms of infection or signs of CSF leakage around insertion site
Assess patient every four hours for signs/symptoms of meningeal irritation
Check integrity of dressing every shift and reinforce if needed
Observe the drainage system, color and clarity of CSF drainage hourly

## Slide 13: Nursing care of the drain
Maintain the integrity and sterility of the closed system by keeping all connections tight
If system becomes disconnected at catheter site, clamp catheter with a sterile clamp and notify physician or nurse practitioner
Assure tubing is not kinked
NEVER INJECT ANYTHING INTO THE SYSTEM

## Slide 14: Troubleshooting the EVD or lumbar drain
No CSF drainage ( < 5ml/hr) when drain open at prescribed level
  Check system integrity for loose connections (never reconnect a broken drain- turn the stop cock proximal to the break to off, cover site with sterile 4x4 and call neurosurgery)
  Confirm all stopcocks open
  Check drain patency by briefly lowering the drain, observe for dripping
  Document troubleshooting measures
  Call neurosurgery if still no drainage

## Slide 15: Serious complications from over-drainage

## Slide 16: What NOT to do…..
Never treat a lumbar drain or EVD like a foley catheter
  Too much drainage can cause intracerebral hemorrhage or herniation
Never disconnect/open the system
  This can cause meningitis, pneumocephalus
Never let patients get out of bed without clamping the system
  Educate patients/families about the dangers of over-drainage
  re-level after all bed adjustments

## Slide 17: Summary
CSF drains are an important treatment strategy for high pressure states and diverting CSF during shunt infection or after durotomy
External sites and drainage must be observed hourly
Care should be taken to maintain the drain at the prescribed level
Patients should be assessed routinely for any change in neurological assessment